## Slide 1: CherryPick: Tracing Packet Trajectory in Software-Defined Datacenter Networks
Praveen Tammana† Rachit Agarwal‡ Myungjin Lee†
†University of Edinburgh ‡UC Berkeley

## Slide 2: Debugging datacenter networks
SDN-enabled datacenters
  Flexible network management
  Control plane policies to data plane rules
  Debugging becomes more challenging
Ensuring data plane conforms with control plane
Notes: .

## Slide 3: Packet trajectory tracing
    “Tracing” the path taken by the packet
      Scalability: Switch flow rules, packet header space
    Policy: All packets from 1 to 3 should go through 4
Actual path : 1 - 6 - 3
mismatch
4
1
2
3
5
6
Checks whether packet followed route as defined in policy
Helps to localize network problems
Ex: misconfiguration, failures

## Slide 4: Enabling packet trajectory tracing
Dst
Src
Insert
ingress link ID
Idea 1: Append link IDs at each hop
User packet
Challenge: Packets traversing non-shortest paths
1
2
3
4
6
Large packet header space
as path length increases
5

## Slide 5: Enabling packet trajectory tracing
Dst
Src
Path id 1
Path id 2
# Switch flow rules ∝ # Paths that contain switch
Idea 2: Maintain global path ID for each unique path
Need one flow rule for
each unique path id
# Paths in 48-ary fat-tree
4 hops : 576 6 hops: 1.3 million !!
Challenge: Packets traversing non-shortest paths

## Slide 6: Existing approaches
Naïve approach
  Switches append ingress link ID into the packet header
  Large number of header bits
PathletTracer [HotSDN’14] and PathQuery [HotSDN’14]
  Switches insert or update path information in packet header
  Large number of switch flow rules
NetSight [NSDI’14]
  Logs packet details at each hop
  Need to collect large amount of data
Topology agnostic
Handles wide range of queries

## Slide 7: CherryPick overview
Exploits the structure in data center topologies
(e.g., fat-tree)
Observation: A small subset of links sufficient to represent any end-to-end path
Scalability:
  Minimal number of flow rules irrespective to path length
  Packet header space requirement is close to state-of-the-art
Notes:   th

## Slide 8: Selectively picking links
Dst
Src
Pick ingress link
Core
Agg
ToR
Only one shortest path from Core to Dst
User packet
All 4 hops: Pick 1 link
id-1
Core
Agg
4 hops
Picked link

## Slide 9: Selectively picking links
Dst
Src
id-1
id-2
Pick ingress link
Only one shortest path between selected links
For more details, please refer to our paper
id-1
All 6 hops: Pick 2 links
Agg
ToR
6 hops
Picked link
Picked link

## Slide 10: Evaluation results for 48-ary fat-tree
ToR Switch
105
107
Header space requirement
is close to PathletTracer
Independent of
path length
Minimal number of switch flow rules

## Slide 11: Conclusion
CherryPick
  Simple and scalable packet trajectory tracing technique
  Demonstrate efficacy under fat-tree topology
  Feasibility: Trace all 4- and 6-hop paths using double tagging
  Low overhead: #OpenFlow rules = #Ports
Future work
  Generalization to other datacenter topologies
  Tracing trajectories of packets that do not reach destination

## Slide 12: Thank You

## Slide 13: Backup-slides
Notes: Spend time on main slide -> more animations, prepare
Keep answer short
Talk & animation should be on sync
Screen wall far – don’t point
General framework :
Start making story and come to point directly

## Slide 14: Selectively picking a minimum number of links
Dst
Src
Pick ingress link
Pick ingress link
id-1
id-3
id-2
Pick ingress link
All 8 hops: Pick 3 links
Notes: Change diagram that embed id’s into pkt header (instead of showing just id’s)
Add bullet points describing technique
Title:
  Exploits topology
Mention path reconstruction